## Slide 1
Report to the WWMIWS-1 Committee: Update on Environment & Climate Change Canada (ECCC) Forecast Service to METAREAs XVII/XVIII & Northwestern METAREA IV (Hudson Bay & Approaches) August 2018 Tom King Marine Sector Specialist Meteorological Service of Canada
Notes: Intro

## Slide 2: METAREAs XVII/XVIII/northwestern IV: Forecast service overview
Forecast bulletins out to Day 2 issued twice daily during the northern/Arctic shipping season (generally runs from June to December depending on known shipping activity);
Promulgated as per GMDSS protocols via Inmarsat-C to Sea Area A3 (south of 75°N) & via HF telex to Sea Area A4 (north of 75°N);
Forecast bulletins also available to internet users via ECCC’s “Datamart” bulletin board & the WWMIWS webpages hosted by Meteo France. .
Notes: M17/18/nw4 forecast service overview.

## Slide 3
Additionally, ECCC has formal agreements with both the U.S. National Weather Service (NWS) & the Danish Meteorological Service (DMI) to act as Preparation Services for U.S. waters within METAREA XVII & Greenlandic waters within METAREA XVIII.
As such, as well as promulgating ECCC forecast products to its assigned METAREAs, ECCC also broadcasts the following international forecast products via Inmarsat-C (sat-c)…
  For U.S. waters within METAREA XVII: FZAK61 PAFG – forecasts for Arctic Alaskan coastal waters; FZAK69 PAFG – forecasts for Arctic Alaskan offshore waters.
  For Greenlandic waters within METAREA XVIII : FBDN51 EKMI – warnings for Greenlandic waters.
METAREAs XVII/XVIII/northwestern IV: Forecast service overview
Notes: M17/18/nw4 forecast service overview.

## Slide 4: New service-related activities for 2018 northern & Arctic shipping season
Removed urgency flags SECURITE & PAN PAN from certain METAREA bulletins as per recommendation of the WWMIWS/ETMSS Chair…
  SECURITE flag – no longer invoked in METAREA bulletins broadcast via sat-c since egc message priority C1 = “1” intrinsically labels such bulletins with “safety” priority, however…
  … SERCURITE flag was retained in bulletins broadcast via HF telex as this medium does not have sat-c’s egc message priority functionality;
  PAN PAN flag – no longer invoked in any METAREA bulletins.. again, egc message priority C1 = “2” intrinsically labels such bulletins as “urgent” priority (i.e. hurricane- force wind warning).
As part of sat-c migration initiative, also used the opportunity to “fine-tune” egc address code C3 in order to reduce excessive broadcast overlap within METAREAs.
Notes: Inmarsat-C migration also provided the opportunity to re-visit original rectangular addressed areas of coverage so as to “fine-tune” egc address code C3 in order to reduce apparent excessive broadcast overlap within METAREAs.
  For bulletins broadcast over sat-c, dissemination system is configured to change egc message priority code C1 from C1 = “1” (safety) to C1 = “2” (urgent) when bulletins carry Hurricane Force Wind Warning.

## Slide 5: New service-related activities for 2018 northern & Arctic shipping season
The modifications to address code C3 raised questions of…
  …recommended amount of address overlap between adjacent METAREAs? (Presuming mariners would want to start receiving the forecasts for adjacent METAREAs prior to actually entering an adjacent METAREA.)
  …when/if the new NAV/METAREAs will be assigned pre-defined addresses represented by the two-digit code & recognized by mini-C receivers? For example, the egc address code C3 for METAREA IV is C3 = “04”.
  Or perhaps Inmarsat has already made such changes? (If so, we’re not aware of it. )
Notes: Questions raised during modifications to egc C3 We’ve increased the longitudinal overlap between those portions of M17 and M18 serviced by sat-c so as to enable vessels steaming at 15 knots to start receiving forecasts for the adjacent METAREA anywhere from 6 to 8 hours prior to entering it.

## Slide 6: New service-related activities for 2018 northern & Arctic shipping season
The modifications to address code C3 also raised questions of…
  How might these new C3 assignments for the new METAREAs impact users with older mini-c receivers?
  Would users have to update their receivers manually to recognize the new C3 codes for the new METAREAs or does Inmarsat somehow provide such receiver updates automatically?
  How much overlap is built into these pre-defined METAREA address codes? (Again, presuming mariners would want to start receiving forecasts for adjacent METAREAs prior to actually entering an adjacent METAREA.)
No doubt something the Inmarsat rep might be able to speak to…in the meantime, rectangular addressing seems to be working fine for the ECCC service.
Notes: New METAREAs are M17/18/19/20/21 We’ve increased the longitudinal overlap between those portions of M17 and M18 serviced by sat-c so as to enable vessels steaming at 15 knots to start receiving forecasts for the adjacent METAREA anywhere from 6 to 8 hours prior to entering it.

## Slide 7: New service-related activities for 2018 northern & Arctic shipping season
Re: sat-c migration.. analysis of POR’s altitude indicated low to nil signal availability to extreme eastern portions of METAREA XVII serviced by sat-c.
Further analysis of sat altitudes indicates maximum coverage to METAREA XVII waters serviced by sat-c will be obtained by broadcasting over both APAC & AMER.
Therefore, upon migration stage 2 (POR to APAC) ECCC plans to upload products for said waters to both AMER & APAC.
However, monitoring of broadcasts over APAC will not be possible at the current ECCC sat-c monitoring receiver sites… analysis of APAC signal coverage from other potential receiver sites within Canada indicates nil signal availability.
This development raises the following question… is an Issuing Service required to monitor broadcasts of its products from each satellite it’s broadcasting over? For ECCC, with regards to any broadcasts made over APAC, this may not be possible.
Notes: Inmarsat-C migration also provided the opportunity to re-visit original rectangular addressed areas of coverage so as to “fine-tune” egc address code C3 in order to reduce apparent excessive broadcast overlap within METAREAs.

## Slide 8: Geo-stationary satellite Elevation Angle – also known as “look angle”.
Angle the geo-stationary satellite will appear above the horizon when viewed from the satellite receiver.
For look angles of zero and less the satellite will be located below the horizon, consequently there will be no signal available to the receiver.
Notes: For sat-c migration, the post-migration look angles for the AMER, APAC, & AOR-E(54) were analysed.

## Slide 9: Look angles for METAREA XVII & XVIII waters serviced by Inmarsat-C
https://www.oceaneering.com/positioning-solutions/geostationary-satellite-calculator/
Notes:   Pre/post-migration look angles for the METAREA XVII & XVIII waters serviced by sat-c.

## Slide 10
Notes:   Pre-migration.. lower signal region exists around the central portion of the Northwest Passage/eastern Prince of Wales Strait & Approaches.

## Slide 11
Notes:   Stage 1 migration results in improved signal coverage over the central portion of the Northwest Passage/eastern Prince of Wales Strait & Approaches, but lowered signal coverage over southeastern METAREA XVIII/western Greenlandic waters.

## Slide 12
Notes:   Stage 2 migration results in lowered signal coverage over southwestern METAREA XVII.

## Slide 13
Notes:   Stage 3 migration results in restored signal coverage over southwestern METAREA XVIII/Bering Strait region.

## Slide 14: Recent challenges encountered with MSI provision or coordination – forecast product-related
Modification of METAREA production software to remove urgency flags SECURITE & PAN PAN inadvertently resulted in temporary loss of some bulletin content…
  the production software was originally configured to use the urgency flags SECURITE & PAN PAN as keywords for the merging process which inserts the ice edge statement into the synopsis section of the bulletins.
  Removal of the urgency flags resulted in the merging script overwriting the first few sections of the bulletins – see examples in following slides.
Notes: Challenges encountered this shipping season – side-effects from urgency flag removal was probably the most significant… required quick response.

## Slide 15
Example of product-related challenges encountered with MSI provision or coordination
METAREA bulletin after production software was modified to remove urgency flags SECURITE & PAN PAN – note the WMO telecomm header is immediately followed by the ICE EDGE statement; the title-block, warnings section & synopsis section are missing:
Notes: Example of missing bulletin sections due urgency flag removal as merging script keyword.

## Slide 16
Example of product-related challenges encountered with MSI provision or coordination
METAREA bulletin upon fixing merging script so as to accommodate loss of the urgency flags SECURITE & PAN PAN – note the restored sections that had previously been stripped out due to loss of the urgency flags as keywords in the merging script:
Notes: Example of restored bulletin sections.. so needless to say there was much flurry of activity to resolve this issue ASAP.

## Slide 17: Recent challenges encountered with MSI provision or coordination – forecast product-related
Potential for such side-effects prior to the modification was known & raised,
However, program discontinuities resulting from retirements/staff re-assignments resulted in these concerns not being realized until production for the 2018 shipping season had already commenced.
Therefore, staffing issues such as retirements/staff re-assignment may also pose a challenge to the operation & maintenance ECCC’s METAREA program this year.
The seasonal, discontinuous nature of the service itself may also be an aggravating factor.
Notes: Challenges encountered this shipping season – side-effects from urgency flag removal was probably the most significant… required quick response.

## Slide 18: Recent challenges encountered with MSI provision or coordination – ice product-related
Some issues were also noted with METAREA ice products…
  The FICN36/96 CWIS ice NAVTEX was having content issues… some zones were duplicated while others were missing.
  Inconsistent ice info between bulletins… the ice-edge statement in the FQCN05 CWAO bulletin for northwestern METAREA IV – Hudson Bay & Approaches – stated “ice-covered”, however, the FICN05 CWIS ice-info bulletin for the same region has much open water throughout the marine district.
  CIS development team quickly resolved these issues upon being notified.
CIS development team has also implemented ETMSS directive on removal of urgency flags from METAREA ice information bulletins broadcast via Inmarsat-C.
Needless to say… these various product-related issues highlight the need for vigilant product monitoring.
Notes: Additional challenges re: ice-related… some issues noticed with METAREA ice bulletins.

## Slide 19
Example of product-related challenges… FICN36 CWIS with duplicated/missing zones (left) & correct version (right).
Notes: Examples of issues noted with METAREA ice bulletins – NAVTEX missing/duplicated zones.

## Slide 20
Example of product-related challenges - inconsistent ice info between METAREA marine forecast & ice bulletins
Notes: Examples of issues noted with METAREA ice bulletins – conflicting ice-edge info.

## Slide 21: Recent challenges encountered with MSI provision or coordination – dissemination-related.
DMI products were missing for a period of time over winter & spring 2018 – issue was on DMI’s end & was eventually resolved, however, reason for loss of feed remains unclear… DMI “…had to do a complete re-installation of the scripts handling the files..”
METAREA XVII – the FZAK61 PAFG was missing from the GTS during the earlier part of the shipping season…
  Inquires made to both Fairbanks & the ECCC Dissemination Unit;
  the bulletin reappeared on July 16; again, unsure of what caused the bulletin to go missing or become available again.
Northwestern METAREA IV –
  Occasional missing bulletins for Hudson Bay on the JCOMM/WWMIWS webpage…
  … inquiries were made to host administrator Meteo France – issue did not originate on their end.
  Issue appears to sorted itself out… may have been a slow server somewhere in the cloud?
Incidentally, there’s been a noticeable increase in the number of unplanned outage notifications from Inmarsat this year… something to do with sat-c migration perhaps?
Notes: Some issues noted involving bulletins apparently gone AWOL.

## Slide 22: Significant examples of stakeholder interactions or education activities
Canadian Marine Advisory Council (CMAC) holds regional meetings on an annual basis for stakeholders & marine interests including northern/Arctic shipping.
The northern/Arctic meeting is co-chaired by the Canadian Coast Guard.
ECCC reps from both MSC & CIS routinely attend this meeting to discuss forecast & ice service-related issues with stakeholders/shippers & to respond to any queries they may have.
Notes: From METAREA self-assessment… ECCC routinely sends representatives from both the Meteorological Service of Canada (MSC) and the Canadian Ice Service (CIS) to the annual Canadian Marine Advisory Council (CMAC) meeting for Prairie & Northern Region, held on an annual basis and chaired jointly with the Canadian Coast Guard (CCG). Additionally, the MSC Marine Sector Specialist met with the CCG NAVAREA coordinator in March 2018 to discuss issues related to NAV/METAREAs and the MSC Marine & METAREA Forecast Programs. The Marine Sector Specialist maintains regular contact with the CGG NAVAREA coordinator relating to joint NAV/METAREA issues.

## Slide 23: Significant examples of stakeholder interactions or education activities
Joint initiative between the CIS & CCG… newly-trained Ice Service Specialists (ISS) graduated Spring 2018.
The ISS were deployed on CCG vessels sailing out of Vancouver & Newfoundland assigned to northern/Arctic patrol.​
The ISS will add extra information to obs coming from CCG ships including sky condition, visibility, precipitation & sea-surface temperature.
Additionally, interaction on a regular basis with NAVAREA XVII/XVIII coordinator on MET/NAVAREA-related issues as well as “domestic” marine program issues.
Notes: From METAREA self-assessment… Additionally, to address needs for capacity building in the marine forecast & sea-ice information programs, a recent exercise in inter-agency capacity building involved a joint initiative between the Canadian Ice Service (CIS) and the CCG, whereby newly-trained Ice Service Specialists (ISS) graduated in Spring 2018 for deployment aboard CCG vessels sailing out of Vancouver & Newfoundland assigned to northern/Arctic patrol. This new crop of ISS staff will add extra information to marine weather observations from CCG vessels navigating ECCC-assigned METAREA waters including sky condition, visibility, precipitation & sea-surface temperature.

## Slide 24
Thank you
Merci
Notes: Thans you /Merci

## Slide 25: Acronyms used in this presentation: CCG – Canadian Coast Guard CIS – Canadian Ice Service DMI – Danish Meteorological Service ECCC – Environment & Climate Change Canada egc – enhanced group call GTS – Global Telecommunications System MSC – Meteorological Service of Canada NWS – National Weather Service sat-c – Inmarsat-C
Notes:   Acronyms list